## Slide 1: Managing an IoT System Haystack Compliance and Efficient Data Retention
Haystack In Practice
Corbyn Knotts
Paul Grinberg
Notes: paul.Grinberg@daikinapplied.com

## Slide 2: Efficient Device Communication
Device 1 (Flat)
OAT
OAT_Units
Device 2 (BACnet)
OA_TEMP
Present_Value
Units
Device 3 (Hierarchy)
OA_TEMP
PVal
Unit
Cloud has little control over devices
Devices prefer certain communication format
Cloud contextualization may have introduce errors
Notes: Paul -
Talking Points
Different device communication protocols have their nuances that may imply structure
Bullet 1
devices connecting to the cloud can be anything (old/new/internal/3rd party).
Cloud cannot mandate 100% of how data should be communicated.
Bullet 2
Embedded devices have their “preferred” way to communicate stemming from how they keep track of data.
For example, some devices may consider “units” as data, while others may treat is as metadata
Bullet 3
Even if possible, forcing conformity may have unintended “context” problems
There is value in the cloud to retaining native structure
  Allows access in native format
  Allows cloud to make decision based historic changes in native format
Why? – Users and process of information in the cloud typically “just want the value”.

## Slide 3: Atomic Information Storage
Device 1 (Flat)
OAT
OAT_Units
Device 2 (BACnet)
OA_TEMP
Present_Value
Device 3 (Hierarchy)
OA_TEMP
PVal
Unit
Data Id
Value
Data Storage
Units
Values are generic
Every “value” has an Id
Single Storage Format
Notes: Corbyn –
Talking Points
Bullet 1 – A value is whether it be meta data, context, or sensor reading need to be accessibly atomically.
Sensor
Point
Metadata
Context
Bullet 2 – Minutia details of how the value became available are irrelevant at a high level.
No relation between values
Unique Identifier is created for
Bullet 3 – Storage supports a standard format that requires only
Unique ID
The Value
Why? – Users and process of information in the cloud typically “just want the value”.

## Slide 4: Atomic Information Access
Device 1 (Flat)
OAT
OAT_Units
Device 2 (BACnet)
OA_TEMP
Present_Value
Device 3 (Hierarchy)
OA_TEMP
PVal
Unit
Data Id
Standard Value
Data Storage
Units
Native Value
Notes: Paul –
Need to present values to users in a way that makes sense to them
Device engineers prefer the native values
Some cloud processes prefer standard values, but benefit from the extra information from native value
Need to balance the needs of
efficient communication from devices
efficient storage of native data
efficient access of standardized data
In other words, we need both formats – but that’s inefficient

## Slide 5: Structed Data Access
Point
Tag
Value
Tag
Value
DataId
DataId
DataId
Data Storage
Haystack Structure
Point
Member
Value
Member
Property
Native Structure
Value
Notes: Corbyn -
Application, integrators, user can be concerned with Haystack structure to access data
Engineers, data analysts, product development will want to access data in the native structure.
We do not duplicate data: 2 points of access to same Data Id
Resolves data conflicts
Haystack Structure

## Slide 6: How can we achive this?
"All problems in computer science can be solved by another level of indirection.“
- David Wheeler
https://en.wikipedia.org/wiki/David_Wheeler_(computer_scientist)#cite_note-26
Notes: Paul -

## Slide 7: Storage Abstraction Needed
DataId
DataId
DataId
Data Storage
?
Haystack Entity Model
Point
Haystack Tag
Haystack Tag
Notes: Paul -
Need some way to decouple the Haystack Entity Model from the underlying DataIDs in the storage
This needs to be generic, auto-computed, short lived, without data duplication, cost efficient (CPU and storage)

## Slide 8: Referential Storage Abstraction
Point
Value Tag
Source
Value Tag
Source
DataId
DataId
DataId
Data Storage
Referential Storage
Haystack Entity Model
Point
Haystack Tag
Haystack Tag
Notes: Corbyn -
Haystack Entity Model
  Are maintained and reviewed
  Can be swapped out if new or different models are aggreged upon
Referential Storage
  only created as needed based on logic in place
  No History for referential storage by design to honor current tags describing current state (history of tag changes can be tracked via an independent process.
  Logic is created to allow for automated mapping to be performed and is defined on many levels as needed
    Protocol (BacNet – StateText to enum)
    Model
    Existing tags
  If there is no data source for a value tag it is not created in referential storage
  Logic runs on all applicable “Events”
    Updates to Haystack entity models
    New data point
    Update to data point value (*if defined by logic)
Value Tags
  Can be Reference a Haystack Entity Model tag. If a Value tag does not reference a Haystack Tag is will not be used when haystack complaint query is performed.
    There are still marker tags and other value tags available for the point

## Slide 9: Workflow
Create
Haystack
Model
Referential Storage
Create
Native
Model
Associate
Native to Haystack Model
Communicate
Values
Cloud stores
As DataID
Communicated Values
Available to
Users by
Haystack or
Native format
Notes: Corbyn –
Yellow – Models created and managed “globally” we do not
Red – Referential storage is short lives and created as needed – is used to create haystack model for user consumption (model itself is no stored for a specific instance)
Green – Data storage – Long Lived historical storage if “value” event, non-relational (help keep cost and query time down)

## Slide 10: Use Case 1 – We now know more!
A group of devices has been sending data
We just learned more about how to understand data
Engineering units are now known
Haystack tags are now known
There is no need to re-generate nonvolatile storage
Native data format still available
Referential storage is dynamically updated as needed
Notes: Paul

## Slide 11: Use Case 2 – Support new equipment
We have user applications based off Haystack models
An equipment is connected that does not match any existing model mapping
The Native model will be created automatically
Association between this new native model to the Haystack model will be done
The Equipment will be fully functional in user applications
History is stored even if we do not yet have a Haystack model for an equipment
Haystack model is referential and will work for data sent before it was created
Haystack model will be automatic for all future equipment with the same native model
Pages and functionality based on Haystack Models
Users do not need to understand native models of equipment to work with equipment
Notes: Corbyn

## Slide 12: Questions?

## Slide 13: Appendix

## Slide 14: Storage Considerations
Haystack Entity Model
Global models available and shareable
Changes may have fundament impact on storage structure
Large amount of same data created for multiple instances
Referential Storage
Short Lived
Quick Access
Does not Contain Values
Describes how to build an entity model
Adaptable to changes or multiple Entity Models
Data Value Storage
Long Lived
Large amount of data
Not Relational
Notes:   Database and data concerns
  Data redundancy
  Retention Polices
  Conflicts
  Database cost and size
  Processing needs

## Slide 15: Single Model Data Storage
Format 2 (BACnet)
OA_TEMP
Present_Value
Units
Format 3 (Properties)
OA_TEMP
PVal
Unit
Standard Format
DataId
Value
Source Content Body
Format 1 (Flat)
OAT
OAT_Units

## Slide 16: Single Value Data Storage
DataId
DataId
DataId
Data Storage
Format 2 (BACnet)
OA_TEMP
Present_Value
Units
Format 3 (Properties)
OA_TEMP
PVal
Unit
Format 1 (Flat)
OAT
OAT_Units