## Slide 1: Energy Analyst - Using Haystack for Real Time Grid Integration
Business Track
Philip Buonomo – VP Product Development, Intellastar

## Slide 2
Intellastar T350
M
ISO/RTO
Grid APIs
Solar Xeto Lib
Battery Xeto Lib
HVAC Xeto Lib
Energy Metering
Xeto Lib
EV Xeto Lib
OCPP
Modbus, BACnet, etc
Modbus, BACnet, etc
Sunspec
Modbus
Generation Xeto Lib
Customer Cloud
Energy Analyst

## Slide 3: Energy Markets 101
ISO / RTO | Areas Served | Approximate Peak Demand | Approximate Customers
PJM | Mid-Atlantic and Midwest | 165,492 MW | 65 million
MISO | Midwest and Southern U.S. | 127,125 MW | 42 million
CAISO | California | 50,270 MW | 32 million
NYISO | New York State | 32,076 MW | 19.8 million
ISO-NE | New England states | 28,130 MW | 14.8 million
ERCOT | Most of Texas | 80,200 MW | 26 million
SPP | Central U.S. | 51,000 MW | 18 million

## Slide 4: Energy Markets 101
Day-Ahead Markets: In the day-ahead market, electricity is traded one day before it is actually consumed.
Real-Time Markets: The real-time market operates on a much shorter interval, typically every five to fifteen minutes, to ensure continuous balance and address fluctuations in demand or supply.
Capacity Markets: Capacity markets ensure that there is sufficient generation capacity available to meet peak demand in the future.
Locational Marginal Pricing (LMP): LMP is a pricing mechanism that reflects the value of energy at different locations, considering the cost of delivering electricity, transmission congestion, and losses.

## Slide 5: Energy Value Stacking
Strategy | Objective | Common Use Case
Day-Ahead Market Optimization | Reduce procurement costs by buying in advance | Facilities with energy procurement flexibility
Real-Time Price Response | Adjust load in response to 5–15 min price updates | High-load facilities with automation systems
Capacity Management (ICAP/5CP/4CP) | Reduce future year capacity obligations during peak intervals | Predictive load shedding during peak forecasts
Demand Response (Emergency/Economic) | Earn revenue or savings by curtailing load during grid stress | Industrial or commercial buildings with curtailable load
Load Shifting via TOU Tariffs | Shift usage from on-peak to off-peak periods | Manufacturing or HVAC load optimization
Participation in Deregulated Markets | Negotiate better contracts, reduce risk | Large buyers in deregulated states
Renewable & Storage Dispatch | Maximize use of DERs to avoid grid purchases | Sites with solar PV, battery storage, or EV infrastructure
Virtual Power Plant Aggregation | Monetize DER coordination through market participation | Multi-site portfolios or large campuses with DERs

## Slide 6: How we Use Haystack
6
Model-driven analytics, user experience, and APIs
Model-driven data ingestion & normalization
Model-driven controls and automation

## Slide 7: Grid Integration

## Slide 8: Energy Analyst Benefits at Scale
Economic Impact: Reduced utility spend, avoided capital expenses, better rate plans, or revenue from grid services.
Carbon Reduction: Emissions avoided through reduced usage, smarter procurement, or participation in demand response.
Risk Avoidance: Fewer unplanned outages, improved uptime, and reduced exposure to volatile energy markets or compliance penalties.

## Slide 9: Portfolio Asset Management

## Slide 10: Portfolio Rollup

## Slide 11: Edge Control / Automation

## Slide 12: Economic Impact: PLC Reduction
© 2025 Intellastar Intellectual Property
What is PLC (Peak Load Contribution)?
Determines a site’s share of grid demand during peak periods
Directly impacts capacity charges for the upcoming year
Why It Matters?
Higher PLC → Higher Costs
Lower PLC → More Savings
Haystack modeling of assets to identify optimal strategy for PLC reduction and use stock library of automated controls.

## Slide 13: Risk Avoidance: Feeder Protection
After
Before

## Slide 14: Economic Impact: Generator Utilization

## Slide 15: All of the Above - EV Chargers

## Slide 16: Economic Impact: Load Shifting

## Slide 17: Questions?
Thank you Haystack Connect 2025!